## Slide 1
Soldering Workshop
Kevin Neubauer
Twitter: @kevinneubauer
https://hackaday.io/CircuitsNutsAndBolts
Courseware will be on https://github.com/neubauek

## Slide 2
Workshop Format
Brief Slide Presentation
  Questions At Any Point During Slides
Move To Lab
Assemble Kit
  Questions At Any Point During Assembly

## Slide 3
What is Soldering?
Joining two metal objects by melting a filler between the two
The filler always has a lower melting point than the two objects
“Gluing metal to metal using metal”
Image Source: https://www.kruss.de

## Slide 4
What is Solder?
A metal alloy with a low melting point
Typically comes with some form of cleaning flux embedded in it
  Rosin Core Solder for most uses (including electronics)
  Acid Core Solder for other applications
Image Source: http://www.jtronix.com

## Slide 5
Great! So Why is Soldering Useful?
Electronics
  Repair
  Creation / Prototyping
Plumbing
  “Sweating” Copper
Brazing
  Higher Temp
  Different metals
  “Farm repair”
Stained Glass
Jewelry
Images From:
http://www.kruss.de
http://www.familyhandyman.com
http://allmetalshaping.com
http://www.delphiglass.com

## Slide 6
Tools (For Electronics Soldering)
Soldering Iron and Stand
Solder Sucker
Rosin Core Solder
Diagonal Cutters
Helping Hands
Solder Wick
Images From: www.jtronix.com, www.ebay.com, www.amazon.com, www.sparkfun.com

## Slide 7
Warnings
You are working with very hot temperatures
  Do not touch the metal part of the soldering iron
Fumes are released during the soldering process
  Work in a well ventilated area
Wear safety eye gear
  Clipping component leads can send metal flying
Wash your hands with soap when done
  Most solder is a lead based product

## Slide 8
Process
Clear workspace of unneeded stuff
Put safety glasses on
Heat soldering iron
  For small electronics solder joints, 350-370 degrees Celsius is typically used
Clean iron tip on a brass sponge or damp sponge
“Tin the tip” of the iron
  Apply a small amount of solder to the tip
Heat the joint to be soldered
  Be sure tip of iron is touching both the component lead and the solder pad
Image Source: http://learn.adafruit.com

## Slide 9
Process (continued)
Apply solder to pad and component lead
  Let it flow into the joint until it is slightly overfilled
Remove soldering iron from joint
Let joint cool for a couple seconds without disturbing it
  Disturbing joints while still hot makes “cold solder joints”
Clip the component lead with diagonal cutters
Image Source: http://learn.adafruit.com

## Slide 10
Finished Results
Image Sources: http://learn.adafruit.com and http://www.mtarr.co.uk/courses/topics/0170_wsp/

## Slide 11
Some Common Problems
Image Source: http://learn.adafruit.com
Solder Bridge
Too Hot
“Cold” Joint

## Slide 12
More Info on Electronics Soldering
Adafruit Learning Site
  http://learn.adafruit.com
Adafruit Tutorial on Soldering
  https://learn.adafruit.com/adafruit-guide-excellent-soldering/
Sparkfun Learning Site
  https://learn.sparkfun.com
Sparkfun Tutorial on Soldering
  https://learn.sparkfun.com/tutorials/how-to-solder---through-hole-soldering
Instructables – Search for “how to solder”
  http://www.instructables.com
YouTube – Search for “how to solder”
  http://www.youtube.com

## Slide 13
Sources for Materials, Tools, Kits
http://www.adafruit.com And http://www.sparkfun.com
  Great electronics hobbyist sites with tools, kits, and ready made Arduino and Raspberry Pi compatible modules
  Many educational articles
  Both actively contribute to Open Source Hardware (OSHW) movement
http://www.amazon.com
  Good for budget tools and materials (read reviews)
http://www.ebay.com
  When you want really cheap Chinese stuff and you don’t read Mandarin
  Some US sellers for kits and tools but mostly international
  You get what you pay for / Don’t expect quality goods or fast ship times

## Slide 14
Questions?